## Slide 1: To Cross, or Not to Cross Pages for Prefetching?
1Huawei Technologies 2Barcelona Supercomputing Center 3University of Edinburgh
Georgios Vavouliotis1 Marti Torrents2 Boris Grot1,3 Kleovoulos Kalaitzidis1 Leeor Peled1 Marc Casas2
— Huawei Confidential —

## Slide 2: Hardware Prefetching in Post-Moore Era
Free lunch is over!
Hardware Prefetching dominates IPC uplifts between processor generations
 | IPC Uplift (%)
HW Prefetching | 5.3%
Total | 13.0%
40%
CORE
DRAM
L1C
L2C/LLC
Pref
Pref

## Slide 3: Hardware Prefetching and VIPT Caches
HW prefetchers for VIPT caches drive prefetching with v@
Prefetch requests need to go through the TLB hierarchy

## Slide 4: Hardware Prefetching and VIPT Caches
HW prefetchers for VIPT caches drive prefetching with v@
Prefetch requests need to go through the TLB hierarchy
  If translation is stored in TLB  issue cache prefetch
TLB HIT

## Slide 5: Hardware Prefetching and VIPT Caches
HW prefetchers for VIPT caches drive prefetching with v@
Prefetch requests need to go through the TLB hierarchy
  If translation is stored in TLB  issue cache prefetch
  What if the translation is NOT stored in TLB?
Trigger page walk to fetch the translation
  Prefetching timeliness
  TLB/Cache pollution
  Energy overhead
Discard page-cross prefetch request
  Sub-optimal performance gains
  Safest option
TLB MISS

## Slide 6: Mismatch Between Academia and Industry
Academia
Typically proposes prefetch engines that target in-page patterns
  Capture more patterns than prior prefetcher designs1,2
Neglect page-cross prefetching
Industry
Optimize prefetching for both in-page and cross-page patterns3
No additional information provided
  Permit all page-cross prefetches?
  Dynamically optimize decisions?
1Berti: an Accurate Local-Delta Data Prefetcher, MICRO’22
2Bouquet of Instruction Pointers: Instruction Pointer Classifier-based Spatial Hardware Prefetching, ISCA’20
3

## Slide 7: Mismatch Between Academia and Industry
Academia
Typically proposes prefetch engines that target in-page patterns
  Capture more patterns than prior prefetcher designs1,2
Neglect page-cross prefetching
Industry
Optimize prefetching for both in-page and cross-page patterns3
No additional information provided
  Permit all page-cross prefetches?
  Dynamically optimize decisions?
We analyze page-cross prefetching across various cache prefetchers
We show that constantly permitting page-cross prefetching provides suboptimal gains
We propose a prefetcher-agnostic scheme to optimize prefetching across page boundaries
We call architects to pay more attention to page-cross prefetching
1Berti: an Accurate Local-Delta Data Prefetcher, MICRO’22
2Bouquet of Instruction Pointers: Instruction Pointer Classifier-based Spatial Hardware Prefetching, ISCA’20
3

## Slide 8: Static Policies are Suboptimal
Chart: Benchmarks from SPEC 2006, SPEC 2017, GAP, PARSEC, LIGRA, CVP1, GeekBench
| mcf | libquantum | astar | sphinx3 | xalan | mcf_s | gcc_s | bwaves_s | imagick_s | fotonik3d_s | bc.web | bfs.web | cc.road | pr.web | tc.road | BF | CF | MIS | dedup | facesim | vips | streamcluster | qmm_int_13 | qmm_int_365 | qmm_int_428 | qmm_int_434 | qmm_int_769 | qmm_int_859 | qmm_int_952 | qmm_int_953 | qmm_fp_12 | qmm_fp_44 | qmm_fp_60 | qmm_fp_84 | gkb5_101 | gkb5_301 | gkb5_306 | gkb5_310 | GeoMean
Berti+Permit Page-Cross | -4.6 | 2.7 | 6.6 | -3.6 | -7.1 | -8.2 | 0.4 | 1.3 | 1.2 | -6 | -12.6 | 4.5 | 10.3 | -4.2 | 4.1 | 2.5 | 9.9 | 7.5 | 0.3 | 2.2 | 5.7 | -3.2 | 9.9 | 10.8 | -21.9 | 6.9 | -17.9 | -9.9 | -18.7 | 5.9 | 5.7 | -9.9 | 2.4 | -8.1 | 22.7 | -13.6 | 7.5 | -7.6 | -1.6
1Berti: an Accurate Local-Delta Data Prefetcher, MICRO’22

## Slide 9: Static Policies are Suboptimal
Chart: Benchmarks from SPEC 2006, SPEC 2017, GAP, PARSEC, LIGRA, CVP1, GeekBench
| mcf | libquantum | astar | sphinx3 | xalan | mcf_s | gcc_s | bwaves_s | imagick_s | fotonik3d_s | bc.web | bfs.web | cc.road | pr.web | tc.road | BF | CF | MIS | dedup | facesim | vips | streamcluster | qmm_int_13 | qmm_int_365 | qmm_int_428 | qmm_int_434 | qmm_int_769 | qmm_int_859 | qmm_int_952 | qmm_int_953 | qmm_fp_12 | qmm_fp_44 | qmm_fp_60 | qmm_fp_84 | gkb5_101 | gkb5_301 | gkb5_306 | gkb5_310 | GeoMean
Berti+Permit Page-Cross | -4.6 | 2.7 | 6.6 | -3.6 | -7.1 | -8.2 | 0.4 | 1.3 | 1.2 | -6 | -12.6 | 4.5 | 10.3 | -4.2 | 4.1 | 2.5 | 9.9 | 7.5 | 0.3 | 2.2 | 5.7 | -3.2 | 9.9 | 10.8 | -21.9 | 6.9 | -17.9 | -9.9 | -18.7 | 5.9 | 5.7 | -9.9 | 2.4 | -8.1 | 22.7 | -13.6 | 7.5 | -7.6 | -1.6
1Berti: an Accurate Local-Delta Data Prefetcher, MICRO’22

## Slide 10: Static Policies are Suboptimal
Chart: Benchmarks from SPEC 2006, SPEC 2017, GAP, PARSEC, LIGRA, CVP1, GeekBench
| mcf | libquantum | astar | sphinx3 | xalan | mcf_s | gcc_s | bwaves_s | imagick_s | fotonik3d_s | bc.web | bfs.web | cc.road | pr.web | tc.road | BF | CF | MIS | dedup | facesim | vips | streamcluster | qmm_int_13 | qmm_int_365 | qmm_int_428 | qmm_int_434 | qmm_int_769 | qmm_int_859 | qmm_int_952 | qmm_int_953 | qmm_fp_12 | qmm_fp_44 | qmm_fp_60 | qmm_fp_84 | gkb5_101 | gkb5_301 | gkb5_306 | gkb5_310 | GeoMean
Berti+Permit Page-Cross | -4.6 | 2.7 | 6.6 | -3.6 | -7.1 | -8.2 | 0.4 | 1.3 | 1.2 | -6 | -12.6 | 4.5 | 10.3 | -4.2 | 4.1 | 2.5 | 9.9 | 7.5 | 0.3 | 2.2 | 5.7 | -3.2 | 9.9 | 10.8 | -21.9 | 6.9 | -17.9 | -9.9 | -18.7 | 5.9 | 5.7 | -9.9 | 2.4 | -8.1 | 22.7 | -13.6 | 7.5 | -7.6 | -1.6
1Berti: an Accurate Local-Delta Data Prefetcher, MICRO’22
Constantly permitting or discarding page-cross prefetching provides suboptimal gains
Chart: Percentage of Page-Cross Prefetches (%)
| avg
Useful Page-Cross Prefs | 57
Useless Page-Cross Prefs | 43
>40% of the page-cross prefetches are inaccurate
Can we filter out the useless page-cross prefetches?

## Slide 11: MOKA: A Framework for Designing Page-Cross Filters

## Slide 12: MOKA: A Framework for Designing Page-Cross Filters
TLB
L1D
L2C/LLC/DRAM
HW
Pref
Page-Cross Filter
Page
Cross?
yes

## Slide 13: MOKA: A Framework for Designing Page-Cross Filters
TLB
L1D
L2C/LLC/DRAM
HW
Pref
Page-Cross Filter
Page
Cross?
Permit?
no
yes
yes
Discard

## Slide 14: MOKA: A Framework for Designing Page-Cross Filters
TLB
L1D
L2C/LLC/DRAM
HW
Pref
Page-Cross Filter
Page
Cross?
Permit?
no
yes
Discard
yes
Program Features
System Features
Virtual Update Buffer (vUB)
Physical Update Buffer (pUB)
Adaptive
Scheme
WTN
Wi
WT1
Wi
…
Weight Tables storing perceptron weights
vUB | 
v@ | hash
False positive detection: stores predicted to be useless page-cross prefetches
SF1
SFN
…
Take into account system state on decision making
pUB | 
p@ | hash
stores issued page-cross prefetches
Page Cross Bit (PCB)
Epoch-based scheme that uses runtime information to tune activation threshold

## Slide 15: DRIPPER: A Page-Cross Filter Prototype
MOKA framework comes with a set of program features and system features
Offline exploration of features
  Optimization metric  IPC speedup
Considered prefetchers  Berti1, IPCP2, BOP3
 | Selected Features | DRIPPER’s Storage Overhead
Berti | Delta, TLB MPKI, TLB MissRate | 1.5KB
BOP | PC^Delta, TLB MPKI, TLB MissRate | 1.5KB
IPCP | PC^Delta, TLB MPKI, TLB MissRate | 1.5KB
1Berti: an Accurate Local-Delta Data Prefetcher, MICRO’22
2Bouquet of Instruction Pointers: Instruction Pointer Classifier-based Spatial Hardware Prefetching, ISCA’20
3Best Offset Hardware Prefetching, HPCA’16

## Slide 16: Simulation Infrastructure and Workloads
Component | Configuration
Core | 1-8 cores, 4GHz, 352e ROB
BP | hashed perceptron
RAS | 64-entry
L1 ITLB | 64-entry, 4-way, 1cc
L1 DTLB | 64-entry, 4-way, 1cc
L2-TLB | 1536-entry, 12-way, 8cc
PT Walker | 4-level split PSC
L1I Cache | 32KB, 8-way, 4cc
L1D Cache | 48KB, 12-way, 5cc
L2 Cache | 512KB, 8-way, 10cc
LLC | 2MB, 16-way, 20cc
DRAM | 4GB (1-core), 16GB(8-core)
ChampSim simulator
  1-core and 8-core experiments
  5-level radix-tree page table
  Page sizes: (1) 4KB (2) 4KB+2MB
Workloads
  Training Set (218 workloads)
  Validation Set (178 workloads)
Benchmark Suites
SPEC CPU 2006
SPEC CPU 2017
GAP
LIGRA
PARSEC
GeekBench5
CVP-1 INT, FP
Benchmark Suites | 
SPEC CPU 2006 | PARSEC
SPEC CPU 2017 | GeekBench5
GAP | CVP-1 INT, FP
LIGRA | 

## Slide 17: Performance Evaluation
Chart: Benchmarks from SPEC 2006, SPEC 2017, GAP, PARSEC, LIGRA, CVP1, GeekBench
DRIPPER provides significant IPC uplifts across different prefetchers
Chart: GeoMean IPC Speedup (%) over Berti + Discard Page-Cross
| Berti
Berti+Permit Page-Cross | -0.7
Berti+DRIPPER | 1.8
Berti+PPF | -0.3
Chart: GeoMean IPC Speedup (%) over Discard Page-Cross
| Berti | BOP | IPCP
Permit Page-Cross | -0.7 | -0.6 | -1
DRIPPER | 1.8 | 0.7 | 1.1
PPF | -0.3 | -0.4 | -0.3
Chart: GeoMean IPC Speedup (%)
| Berti
Berti+Permit Page-Cross | -0.7
Berti+DRIPPER | 1.8
1Perceptron-Based Prefetch Filtering, ISCA’19
1
1

## Slide 18: Why DRIPPER Provides Benefits?
DRIPPER has similar coverage to Permit Page-Cross
DRIPPER has higher accuracy than Permit Page-Cross
DRIPPER has positive impact on DTLB MPKI
DRIPPER has positive impact on L1D MPKI

## Slide 19: Additional Evaluation
Multi-core evaluation
Impact on the validation set of workloads
Evaluation when multiple page sizes are used
Comparison between system features and program features
Evaluation across different L2C prefetchers

## Slide 20: Putting Everything Together
DRIPPER: A Page-Cross Filter Prototype
  IPC gains across different prefetchers and benchmark suites
  Small storage overheads
Prefetching beyond page boundaries needs more attention
Static policies for page-cross prefetches are suboptimal
Big fraction of page-cross prefetches are inaccurate
MOKA: A Framework for designing Page-Cross Filters

## Slide 21
ZURICH RESEARCH CENTER
Copyright © Huawei Technologies Switzerland AG. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
THANK YOU

## Slide 22
ZURICH RESEARCH CENTER
Copyright © Huawei Technologies Switzerland AG. All Rights Reserved.
The information in this document may contain predictive statements including, without limitation, statements regarding the future financial and operating results, future product portfolio, new technology, etc. There are a number of factors that could cause actual results and developments to differ materially from those expressed or implied in the predictive statements. Therefore, such information is provided for reference purpose only and constitutes neither an offer nor an acceptance. Huawei may change the information at any time without notice.
Backup Slides

## Slide 23: Usefulness of Page-Cross Prefetching

## Slide 24: Page-Cross Filter – Prediction
Page-Cross Filter
WTN
Wi
WT1
Wi
…
SF1
SFN
…
F1
#
FN
#
>Tact
L1D
L2C/LLC/DRAM
yes
Discard
no

## Slide 25: System Features
L2-TLB MPKI
  Targets phases with low L2-TLB MPKI
    High probability for a page-cross prefetch to hit in TLB
    Make DRIPPER more aggressive during these phases
L2-TLB Miss Rate
  Targets phases with high L2-TLB pressure
  Idea  most demand L2-TLB accesses are misses
    Try if page-cross prefetching can reduce the pressure
  Miss rate is more sensitive to changes than MPKI

## Slide 26: Detailed Storage Overhead of DRIPPER
 | Storage Overhead
Program Features | 0.625KB
System Features | 0.00125KB
vUB/pUB | 0.024KB/0.768KB
Total | 1.44KB

## Slide 27: 8-core Evaluation

## Slide 28: IPC Gain Breakdown